DU-V88.DOC
			      ----------

		By Ward Christensen (revised 05/14/84)
additional notes by Ron Fowler, Irv Hoff, and Jeffrey Nonken, C.B Falconer

This version of DU is compatible with CP/M 2.x and 3.x and does not require
require alteration for various hardware configurations.   It adjusts itself
automatically to the correct number of sectors, tracks, directory size etc.


				 INDEX

		   1.0	   INSTALLATION:
		   2.0	   USE:
		   2.1	   COMMANDS, BY FUNCTION
		   2.2	   ALPHABETIC COMMAND SUMMARY
		   3.0	   NOTES
		   4.0	   INTERPRETATING DIRECTORY DATA
		   4.1	   SINGLE DENSITY
		   4.2	   DOUBLE DENSITY



1.0	INSTALLATION:
===
	"DU" should require  no changes  to the source file because of  the
use of  the automatic adaption feature.  The only alteration  that needs to
be done is to use DDT to  set the byte at  103H for your clock speed.   Use
20 for 2MHz, 40 for 4MHz, 60 for 6MHz etc. (This only affects the "Z" SLEEP
command.)


2.0	USE:
===
	To invoke "DU", simply enter "DU" at the CP/M prompt.

	A>DU

	An initial command string may optionally be placed as an operand of
the original "DU" command, i.e.:

	A>DU M;X

for example, if you want to only map the disk, and then exit:


	Once "DU" is running,  it expects single-letter commands  much like
"SID" OR "DDT".   For ease of use,  multiple commands may  be placed on one
line, separated by ";".  In addition, a given command or string of commands
may be repeated  --  either indefinitely  (until ^C is pressed)  or a given
number of times.

	To avoid  an accidental ^C  from dropping  out of  "DU",  only  the
explicit "X" command will exit "DU".


2.1	COMMANDS, BY FUNCTION
===

HELP:
	?	 displays the help guide

POSITIONING:

	Gnn	by allocation group
	Snn	by sector
	Tnn	by track
	+nn	going ahead nn sectors
	-nn	going back nn sectors

I/O:
	<	puts current sector "away" into a buffer
	>	recalls previously saved sector
	Kfn.t	writes "yanked" sectors to a file
		    (see "saving sequential memory" in notes below)
	K	(no operands) resets the "yank" buffer.
	R	reads sector
	W	writes sector
	Y	"yanks" current sector into sequential memory

DISPLAYING:

	#	shows disk parameters
	A	dump sector in ASCII
	D	dump the sector (hex + ASCII)
	G	shows current group, track, sector
	H	dump sector in hex
	M	maps the disk -- where the files are located
	Mxx	map starting at group xx
	Vnn	views (like CP/M type) nn sectors

CHANGING:

	CAnn,VAL change data in ASCII (with <xx> escape to hex)
	CHnn,VAL change data in hex
	Unn	 change user to nn

SEARCHING:

	=Abc	scan for Abc (IN ASCII) from current sector on (very
		    slow, allow up to 15 minutes to scan an entire disk.
		    Either finds the answer or says: "out of bounds".
	FNAME	find a file in the directory
	F	find next occurrence (extent) of same name

MISC:
	(	toggles the map display to show/not show erased files
	/nn	repeat previous command nn times  (repeats indefinitely
		    if nn omitted)
	Bnn	boot nn sectors per track
	LX	log in disk X
	P	printer toggle
	Q	before a command does it "quietly"
	X	exit to CP/M
	Znn	sleep (nn tenths of a second) to allow viewing data
		    before it scrolls off

2.2	ALPHABETIC COMMAND SUMMARY
===

	#	Prints the disk parameters
	+	Advance 1 sector (if below track 2, this advances to
		    next numerical, if 2 or more, advances based on
		    CP/M"s normal sector scrambling algorithm, i.e.,
		    allows + to the next logical sector of the file.
	-	backs up 1 logical sector
		    NOTE:  + and - may take an amount:	For example,
			   +15 advances 15 sectors
	/	repeats entire command -- defaults to "forever"
	/nn	nn may be 2 TO 65535
	(	toggles the map display to show/not show erased files.
		    When showing erased files "*" indicates that block
		    duplicates a block in another file.  It may not be
		    possible to restore this program without errors.  If
		    there are no "*" in this complete file, it can be
		    correctly restored.
	<	saves current sector in a "save" buffer
	=Abc	ASCII search, starting at current sector.  <xx> hex
		    may be imbedded or used alone.  To find the ASM
		    instruction: "IN 0FEH"
		    use:  =<DB><FE>  (Ignores bit 7 unless using <xx>.)
		    Since ";" is a command delimiter, you have to use
		    <3B> to search for a ";".  Also, since "<" is a hex
		    escape character, use << to mean a single "<".

		    NOTE:  This is a very slow routine.  It can take 15
			   minutes or longer to search an entire double-
			   density double-sided disk so be patient.  It
			   either finds the string or says:  "OUT OF
			   BOUNDS".
	>	gets saved buffer.  < and > may be used to move
		     a sector to another place.
	?	displays the help guide
	A	dump sector (ASCII only)
	Bnn	boot nn sectors per track -- not all disks have 26.
	CHADDR,VAL,VAL,VAL...	change hex values in sector
	CAADDR,CHAR STRING...	change ASCII calues in sector
		    NOTE:  <xx> may be hex imbedded in the ASCII
			   string:  CA00,OK<0D><0A><1A>
		    ---->  W writes changes to disk
			   note that the "C" command echoes the over-
			   laid data for verification.
	CHADDR-ADDR,BYTE	repeats a change
	CAADDR-ADDR,BYTE	repeats a change
	D	dump sector (hex + ASCII)
	FNAME	print directory for file "NAME"
	F	find next occurrence of name in directory
	Gnn	position to group nn and read
	G	shows current position
	H	dump sector, hex only
	Kdu:filename.ext   save a file from "yanked" sectors.
		    drive, user are optional.  Resets "yank" address.
		    see "saving sequential memory" in notes below.
	K	(no operands) resets the "yank" buffer to empty.
	L	re-logs in the current disk -- you may pull out a
		    disk, put in a new one, and "L" just to log it in.
		    (see "logging in disk" in notes below)
	LX	logs in disk "X", such as: LB, LC, LA, etc.
	M	dumps a map of the group allocations for files
	Mn	shows which file is allocated to group "N"
	N	resets CP/M via BDOS -- this may make it possible under
		    some implementations of CP/M to change the disk
		    format, i.e., density, sides, etc.
	P	toggles the printer on/off
	Q	quiet -- preceedintg any command, suppresses CRT output
	R	reads into memory the sector currently positioned at.
		    NOTE:  "R" (read) is implicit in the G, +, and -
			   commands but NOT in the "S" and "T" commands
	Snn	position to sector nn, and read
	TNN	seek to track nn (no read)
	Ux	logs user "x" for next "F" command
	V	views the current sector -- assumes ASCII data
	Vnn	views nn sectors
	W	writes the current sector to disk
		    NOTE:  may NOT be used after an "F" command as
			   CP/M was used to find file in the directory
	X	exit back to CP/M (must press return).	^C was too
		    easy to hit over modem lines -- requires two bytes:
		    (X,CR) to exit.
	Y	"yank" the current sector into sequential memory
		    (starts at 3000H, increments for each yank)
	Z	sleep -- causes the porgram to pause -- such as to look
		    at a dump.	Z is 1 second
	Znn	nn tenths of a second	Z50 = 5 seconds


3.0	NOTES
===

* Multiple commands:  May be separated by ";"

EXAMPLE:  The following commands will erase the B: disk directory to all
	  E5"s:


	LB		 log in B: drive
	G0		 position to directory
	CH0-7F,E5	 fill with E5
	<		 save the sector
	>;W;+;/16	 restore, write, next, repeat 16


---- this could be shortened to:


	LB;G0;CH0-7F,E5;<
	>;W;+;/16


* DUMP COMMANDS:  All dump commands (D, A, H) may be optionally followed
		  by a starting and ending address:

	D0,7F		 the same as just "D"
	D3,5
	A20,3F


* LOGGING IN DISK:  If you have a disk with a "blown directory" try logging
in a good disk of the same density,  then put in  the "blown"  disk without
logging it in. You are opening yourself to possible problems because of the
buffering of physical sectors in the "BIOS".  The best technique,  (but not
guaranteed), would be to seek to the unused inner tracks of the first disk,
do the read, then change disks.  That way, if it writes anything, you won't
have destroyed anything, assuming the disk is not completely full.  Another
technique  (assuming the second disk does not contain a CP/M system,  would
be to seek to trk 1, do the read there, then change disks to the blown one.


* SAVING SEQUENTIAL MEMORY:
Since CP/M v 3.0 does not have a SAVE function, one has been added.
Syntax is:
	Kdu:filename.ext
	^^^	 ^     ^
	|||	 |     +-- file extension (0-3 characters)
	|||	 +-------- file name (1-8 characters)
	||+--------------- user # (or none)
	|+---------------- drive designation (A-P or none)
	+----------------- DU command

Drive and user may be omitted.	If so, omit the colon as well.   Drive must
be specified if the user is.  If the user # is omitted, the current user is
used.  If the drive is omitted, the current CP/M default drive is used.

This function saves  the current contents of sequential memory into  a disk
file.   The contents  of sequential memory  are determined  by  the  "yank"
function,  and the pointer  of that function is used here.   If nothing has
been yanked,  you get an error.  Once the file has  been saved,  the "yank"
pointer is re-initialized to its original value (3000H). Control is return-
ed to DU.


4.0	INTERPRETATING DIRECTORY DATA
===

4.1	SINGLE DENSITY
===

The following explains the  format of  a CP/M directory entry  as shown  by
"DU", using either the "F" (find file) command, or just doing "D" (dump) of
the directory sectors, which are located in groups 0 and 1 on a single-den-
sity disk.


SAMPLE RESULT OF "FSID.COM" COMMAND:

40  00534944 20202020  20434F4D 0000003A  *.SID     COM...:*
50  33343536 3738393A  00000000 00000000  *3456789:........*


FIRST LINE -

40  00534944 20202020  20434F4D 0000003A  *.SID     COM...:*
||  ||| 		      | ||    ||    |	      |
||  ||^---hex file name/type--^ ||    ||    ^file name^
||  ||				||    ||     in ASCII
||  ||			 extent-^^    ||
||  ||				      ||
||  ||		 file size in sectors-^^
||  ||
||  ^^-00 = file active  other values (E.G 03) = user #
||     E5 = file erased
^^-displacement of line in directory sector


SECOND LINE -

50  33343536 3738393A  00000000 00000000  *3456789:........*
    |				       |   |
    |				       |   ^- allocation groups
    ^-----allocation group numbers-----^	 (just happened to
						 be printable)


4.2	DOUBLE DENSITY
===
	The following is a sample of "FSID.COM" running on a double-
density system:

:FSID.COM
00  00534944 20202020  20434F4D 0000003A  *.SID     COM...:*
10  38003900 3A003B00  00000000 00000000  *8.9.:.;.........*
G=0000:00, T=2, S=1, PS=0


	The primary difference is that the groups now occupy 2 bytes, i.e.,
38 00" "39 00"  ...   this follows the Intel and CP/M convention of putting
16-bit values high-byte-first.	This it means group 0038, 0039 etc.

	Note that  in double-density,  each group stood for 2k, not 1K,  so
there were half as many groups for the same file.

	Be very careful when patching a directory under double-density.
For exmaple:

	CH10,38,39,3A,3B...

	This might try to access group 3938 with resultant angry noise from
the disk stepper as it attempts to find where it should go for the data.
ÄX