Source      :  Amstrad Action
Issue       :  No.19
Date        :  April 1987
Section     :  Programming
Page        :  27

Author      :  AA

There is a simple way of using any standard 5 1/4 inch drive on the 
Amstrad (well, practically any - the author claimed that he haven't
yet found a drive for which this won't work). The cable from the Amstrad
to the drive will need disk-ready line grounded - this can easily be
done by shorting the last two lines together. The simple program 
below should be run before using the drive under Amsdos. It slows the
disc access rates down so that the drive can be used without the ready
line. The drive can also be used under CPM 2.2 by altering the stepping
rates in the SETUP.COM program.

10 PRINT"SETTING DISK RATES FOR 5.25-INCH DRIVE"
20 MEM=HIMEM
30 MEMORY &3000
40 GOSUB 110
50 FOR A=&4000 TO &401F
60 READ N:POKE A,N:NEXT
70 DATA 50,0,250,0,175,30,30,1,1
80 DATA 130,&21,0,&40,&CD,&D4,&BC,&79,&32,&1D,&40,&22,&1B,
   &40,&21,0,&60,&1E,&20,&16,&20,&E,&20,&DF,&1B,&40,&C9,0,
   0,0,0,0,0
90 CALL &4001
100 MEMORY MEM:NEW
110 FOR X=&6000 TO &6008
120 READ D:POKE X,D:NEXT
130 RETURN



There is some disk drive which was recommended by the Amstrad according
to David Robinson in the Amstrad CPC464 User magazine May 1985. One of
the characteristic that 5 1/4 drive must have is:
1) The DRIVE must have a READY signal on pin 34
2) Have suitable step rate, motor on & off timeout.
3) Have a shuggart interface.
The author recommended The CHINNON F051-MD 5/14 disc drive
The next purchase is the power supply providing 12V 5V and ground via a
four pin connector arranged 12V/G/G/5V.
Finally we need a way of connecting the ribbon cable from the disc 
controller to your new disc drive. You need 2 items here:

1. A 34 way card edge connector 
2. A 40 pin PCB header which you convert to 34 ways by cutting off
   three pairs of pins from one end.
Remove the ribbon cable clamp from the card edge connector then carefully
solder the SHORTER of the pins to the terminal on the back.

Where to get this CHINON F 051-MD 5 1/4 inch disk drive here is it:

ALTEK MICROCOMPUTERS LTD.
22 Market Place,
Wokingham,
Berks.

Where to get the power supply:

MICROWORLD.
12 York Place,
Brighton.

Where to get the Connector and cable:

Our local TANDY store.       1) 40 position header - Cat. No. 2761540
                             2) 34 way card edge connector-Cat No. 2761564A

            
I like to advice you that I am not liable to any damage arouse after
this program as I am just provide and information to you. If you like
it keep it if not throw it away. And also there is no guarantee that
this program will work as I haven't test it myself. Thanks.
e is no guarantee that
this program will work as I haven't test it myself. Thanks.